## Slide 1: CHAPTER - 4
Digital Transmission
Part-4

## Slide 2: 4.2 Analog-to-digital conversion
2
There are two techniques
  (1). Pulse Code Modulation (PCM)
  (2). Delta modulation (DM)

## Slide 3: Pulse Code Modulation (PCM)
3
The most common technique to change an analog signal to digital data (digitization) is called pulse code modulation (PCM).
PCM is the preferred method of communication within the public switched telephone network (PSTN).
In PCM, analog signal is sampled and converted to a series of binary bits.
A PCM encoder has three processes.
  (1). The analog signal is sampled.
  (2). The sampled signal is quantized.
  (3). The quantized values are encoded as streams of bits.

## Slide 4: Cont.
4

## Slide 5: Sampling
5
The first step in PCM is sampling.
  It is a process of taking a sufficient number of discrete values at point on a waveform that will define the shape of waveform.
  The more samples you take, the more accurately you will define the waveform.
  It converts analog signal into series of impulses, each representing amplitude of the signal at given point.

## Slide 6: Cont.
6
Before we sample, we have to filter the signal to limit the maximum frequency of the signal as it affects the sampling rate.
Filtering should ensure that we do not distort the signal, i.e. remove high frequency components that affect the signal rate.
The analog signal is sampled every Ts s, where Ts is the sample interval or period.
The inverse of the sampling interval is called the sampling rate or sampling frequency and denoted by fs, where fs = 1/ Ts .

## Slide 7: Cont.
7
There are three sampling methods-ideal, natural, and flat-top-as shown in Figure.

## Slide 8: Cont.
8
Ideal: An impulse at each sampling instant.
Natural: A pulse of sort width with varying amplitude.
Flat-top: Sample and hold, like natural with single amplitude value.
The sampling process is sometimes referred to as pulse amplitude modulation (PAM) and the outcome is a signal with analog (non integer/ non integral) values.

## Slide 9: Cont.
9
Sampling Rate: One important consideration is the sampling rate or frequency. What are the restrictions on Ts?
  This question was elegantly answered by Nyquist. According to the Nyquist theorem, to reproduce the original analog signal, one necessary condition is that the sampling rate be at least twice the highest frequency in the original signal.
According to the Nyquist theorem, the sampling rate must be at least 2 times the highest frequency contained in the signal.

## Slide 10: Cont.
10
We need to elaborate on the theorem at this point.
First, we can sample a signal only if the signal is band-limited. In other words, a signal with an infinite bandwidth cannot be sampled.
Second, the sampling rate must be at least 2 times the highest frequency, not the bandwidth.
  If the analog signal is low-pass, the bandwidth and the highest frequency are the same value.
  If the analog signal is bandpass, the bandwidth value is lower than the value of the maximum frequency.

## Slide 11: Cont.
11
Figure 4.23 Nyquist sampling rate for low-pass and bandpass signals

## Slide 12: Quantization
12
The result of sampling is a series of pulses with amplitude values between the maximum and minimum amplitudes of the signal.
The set of amplitudes values are infinite between the two limits.
We need to map the infinite amplitude values onto a finite set of known values. The following are the steps in quantization:
  1. We assume that the original analog signal has instantaneous amplitudes between Vmin and Vmax
  2. We divide the range into L zones, each of height (delta).
  Δ= (Vmax - Vmin)/ L
  3. We assign quantized values of 0 to L - 1 to the midpoint of each zone.
  4. Each sample falling in a zone is then approximated the value of the mid point.

## Slide 13: Cont.
13
As a simple example, assume that we have a sampled signal and the sample amplitudes are between -20 and +20 V.
We decide to have eight levels (L = 8).
Zone width Δ = (Vmax - Vmin)/ L
Δ =(20-(-20))/8 =5 V.
The 8 zones are: -20 to - 15 , - 15 to -10 , -10 to -5 , -5 to -0 , 0 to +5 , +5 to +10, +10 to +15, +15 to +20.
The midpoints are: -17.5, -12.5, -7.5, -2.5, 2.5, 7.5, 12.5, 17.5

## Slide 14: Cont.
14
Normalized PAM values | -1.22 | 1.50 |  |  |  |  |  |  | 
Normalized Quantized values | -1.5 | 1.5 |  |  |  |  |  |  | 
Normalized error | -0.28 | 0 |  |  |  |  |  |  | 
Quantization code | 2 | 5 |  |  |  |  |  |  | 
Encoded words | 010 | 101 |  |  |  |  |  |  | 

## Slide 15: Cont.
15
Normalized PAM values | -1.22 | 1.50 | 3.24 | 3.94 | 2.20 | -1.10 | -2.26 | -1.88 | -1.20
Normalized Quantized values | -1.5 | 1.5 | 3.50 | 3.50 | 2.50 | -1.50 | -2.50 | -1.50 | -1.50
Normalized error | -0.28 | 0 | +0.26 | -0.44 | +.30 | -.40 | -0.24 | +.038 | -0.30
Quantization code | 2 | 5 | 7 | 7 | 6 | 2 | 1 | 2 | 2
Encoded words | 010 | 101 | 111 | 111 | 110 | 010 | 001 | 010 | 010

## Slide 16: Cont.
16
Normalized PAM values:
We have shown only nine samples using ideal sampling (for simplicity). The value at the top of each sample in the graph shows the actual amplitude. In the chart, the first row is the normalized value for each sample.
PAM= (actual amplitude/Δ)= -6.1/5 = -1.22, …, …,…

## Slide 17: Cont.
17
Normalized Quantized values:
The quantization process selects the quantization value from the middle of each zone. This means that the normalized quantized values (second row) are different from the normalized amplitudes.
(1). -6.1 = -Δ -2 Δ = - 3Δ = -3*5= -15
Middle of zone = (-15/2) = -7.5
= -7.5/ Δ = -1.5
…….., …….. ,…..

## Slide 18: Cont.
18
Normalized Error: The difference between normalized
Quantized values (2nd row) and normalized PAM values (1st row) is called the normalized error (3rd row).
= - 1.5 – (-1.22)= - 0.28, ……, …. , ……
  The value of the error for any sample is less than Δ/2. in other words, we have – Δ/2 ≤ error ≤ +Δ/2.
Quantization code: The fourth row is the quantization code for each sample based on the quantization levels at the left of the graph.

## Slide 19: Cont.
19
Encoded words: The encoded words (fifth row) are the final products of the conversion. After each sample is quantized and the number of bits per sample is decided, each sample can be changed to an nb-bit code word. In Figure 4.26 the encoded words are shown in the last row. A quantization code of 2 is encoded as 010; 5 is encoded as 101; and so on.
  Note that the number of bits for each sample is determined from the number of quantization levels. If the number of quantization levels is L, the number of bits is nb =log2 L.
In our example L is 8 and nb is therefore 3. The bit rate can be found from the formula
Bit rate = sampling rate x number of bits per sample = fs x nb

## Slide 20: Cont.
20
Example 4.14:
We want to digitize the human voice. What is the bit rate, assuming 8 bits per sample?
Solution:
The human voice normally contains frequencies from 0 to 4000 Hz. So the sampling rate and bit rate are calculated as follows:
    Sampling Rate = 4000*2=8000 samples/s
    Bit Rate = 8000*8=64,000bps=64kbps
Nyquist theorem,bit/sampling rate=2*frequency

## Slide 21: Real life Application of Analog-to-Digital conversion
21
H.W

## Slide 22: 4. 3 Transmission Modes
22
The transmission mode decides how data is transmitted between two computers.
The binary data in the form of 1s and 0s can be sent in two different modes: (1). Parallel (2). Serial.

## Slide 23: Parallel Transmission
23
In parallel transmission, multiple bits (usually 8 bits or a byte/character) are sent simultaneously on different channels (wires, frequency channels) within the same cable, or radio path, and synchronized to a clock.
In Parallel Transmission, various bits are sent together simultaneously with a single clock pulse. It is a fast way to transmit as it uses many input/output lines for transferring the data.

## Slide 24: Cont.
24
Simultaneous transmission
Requires separate data lines
Bits must stay synchronized
Fast
Expensive
Example: Printer connections
Transmitter
Receiver
One Word

## Slide 25: Cont.
25
Figure 4.32 Parallel transmission
Figure shows how
parallel transmission
works for n =8.
Typically, the eight
wires are bundled
in a cable with a
connector at each end.

## Slide 26: Examples
26
Examples of parallel mode transmission include connections between a computer and a printer (parallel printer port and cable). Most printers are within 6 meters or 20 feet of the transmitting computer and the slight cost for extra wires is offset by the added speed gained through parallel transmission of data.

## Slide 27: Cont.
27
The advantage of parallel transmission is speed. All else being equal, parallel transmission can increase the transfer speed by a factor of n over serial transmission.
But there is a significant disadvantage: cost. Parallel transmission requires n communication lines (wires in the example) just to transmit the data stream. Because this is expensive, parallel transmission is usually limited to short distances.

## Slide 28: Serial Transmission
28
In serial transmission, bits are sent sequentially on the same channel (wire).
So we need only one communication channel rather than n to transmit data between two communicating devices.
It reduces costs for wire but also slows the speed of transmission.
Each bit has its clock pulse rate.

## Slide 29: Cont.
29
Transmitter
Receiver
One Word
Transfers one bit at a time
Requires only one data line
Bits must stay synchronized
Slow compared to parallel transmission
Less Expensive
Example: USB

## Slide 30: Cont.
30
Figure 4.33 Serial transmission

## Slide 31: Examples
31
Examples of serial mode transmission include connections between a computer and a modem using the RS-232 protocol .

## Slide 32: Cont.
32
The advantage of serial over parallel transmission is that with only one communication channel, serial transmission reduces the cost of transmission over parallel by roughly a factor of n.
Since communication within devices is parallel, conversion devices are required at the interface between the sender and the line (parallel-to-serial) and between the line and the receiver (serial-to-parallel).

## Slide 33: Cont.
33
Serial transmission occurs in one of three ways: (1). Asynchronous (2). Synchronous (3). Isochronous
Serial transmission
Asynchronous
Synchronous
Isochronous

## Slide 34: Asynchronous Transmission
34
Asynchronous transmission sends only one character at a time where a character is either a letter of the alphabet or number or control character i.e. it sends one byte of data at a time.
Bit synchronization between two devices is made possible using start bit and stop bit.
Start bit indicates the beginning of data. A start bit usually 0 is added to the beginning of each byte.
Stop bit indicates the end of data. A stop bit, usually 1 is added to the ending of each byte.

## Slide 35: Cont.
35
Addition of start and stop increase the number of data bits. Hence more bandwidth is consumed in asynchronous transmission.
There is idle time between the transmissions of different data bytes. This idle time is also known as Gap.

## Slide 36: Cont.
36
Figure 4.34 Asynchronous transmission

## Slide 37: Synchronous Transmission
37
Synchronous transmission does not use start and stop bits.
In this method bit stream is combined into longer frames that may contain multiple bytes.
There is no gap between the various bytes in the data stream.
In the absence of start & stop bits, bit synchronization is established between sender & receiver by 'timing' the transmission of each bit.
In order to receive the data error free, the receiver and sender operates at the same clock frequency (Clock signal refers to the electrical pulse that serves as the timing reference for transmission of data.).

## Slide 38: Cont.
38
Figure 4.35 Synchronous transmission

## Slide 39: Isochronous
39
In real-time audio and video, in which uneven delays between frames are not acceptable, synchronous transmission fails.
  For example, TV images are broadcast at the rate of 30 images per second; they must be viewed at the same rate. If each image is sent by using one or more frames, there should be no delays between frames. For this type of application, synchronization between characters is not enough; the entire stream of bits must be synchronized.
The isochronous transmission guarantees that the data arrive at a fixed rate.